HMS LAB HOMEWORK

DUE FEB 19th (2:30pm)

In Table 5.10 on page 351 of Bedient and Huber, there are physical parameters for five watersheds for Keegans Bayou (NOTE: “Channel Length” is really the longest distance from the watershed boundary to the outlet.)

- Use the TC + R values for each subwatershed given in T 5.14 (and calculate yourself later) and set up HEC-HMS according to data provided in text.

| TABLE 5.14 | % Impervious values |
| --- | --- |
| TABLE 5.11 | Rainfall for 3 recording gages |
| TABLE 5.12 | Gage weightings |
| TABLE 5.15b | Routing parameters |
| Table 5.16 | Storage routing data |

- Use “Main” channel for subbasin 2 to route from A to B

- Use “Main” channel for subbasin 3 to route from B to C

- Estimate the relative lengths for “Main” channel in subbasin 4 to route C to D   and then from D to E.

- For the routing steps use Modified Puls

- Assume no Base Flow

- SCS loss rate method with CN of 80

- State all assumptions

- Model the rainfall event for existing conditions.

- Propose and model a new basin model with two detention ponds  (see Case 1 on pages 360 –361 in the text). See table 5.18.

- What hydrologic effect does the pond have on the outlet using the same rainfall?

- Using the base model again from b, evaluate a diversion option from Table 5.20.