## Slide 1: Identifying Flood Risk and Vulnerability
Assessment of the Clear Creak Watershed
Samuel D. Brody, Russell Blessing, Antonia Sebastian, Philip Bedient
Center for Texas Beaches & Shores
Department of Marine Sciences - Galveston
Department of Urban Planning – College Station
Texas A&M University

## Slide 2: Floodplain Management in the U.S.
100-year floodplain guides local and household decisions.
NFIP most widely implemented vehicle:
  >21,000 participating communities
  5.6 million policies, mostly on the coast
From 2000-2005, $19 billion of damage reported through NFIP.

## Slide 3: Limitations of Using the Floodplain
Compounding errors and inconsistencies.
Does not consider effects of land use change.
Environmental and socioeconomic change too rapid.
One percent flood occurring more frequently.
Boundary treated a “dichotomous decision.”

## Slide 4: Disconnect Between Floodplain Boundaries and Actual Loss
Nationwide, 25% of insured claims outside floodplain boundary, 1999-2009.
47% of repetitive flood loss, 54% for Ike in Harris County outside floodplain boundary, 1978-2008.
Chart: 
| A | B | C | X
Paid | 201134551.1184 | 4486589.1864 | 48336101.2059 | 94377374.9179
Notes: More recent analysis of a national sample of 450 jurisdictions showed that approximately 25% of flood insurance claims from 1999 to 2009 were located outside of the 100-year floodplain (Brody and Highfield, 2011).
From 1978 to 2008, we catalogued 9,521 claims over 2,896 properties for a total of approximately $351 million in paid losses. On average, each property in the study area claimed 3.23 losses and received $36,881 per claim. Unexpectedly, we found that over 47 percent of all claims were located outside of the 100-year floodplain boundary. This percentage holds even when examining claims subsequent to the most recent floodplain boundary update in 2007.
In Harris County from 1978 to 2008, we catalogued 9,521 claims over 2,896 properties for a total of approximately $351 million in paid repetitive losses. On average, each property in the study area claimed 3.23 losses and received $36,881 per claim. Almost 35 percent of losses during this period were caused by a hurricane or tropical storm, most recently Hurricane Ike in 2008 which generated $20.4 million in RL damage. Of all losses paid, over 70 percent went to repair building-related damage (versus contents) of which 94 percent was from single family structures. Houston incurred by far the largest amount of total flood loss. But, on a per claim basis, the cities of La Porte and Webster ranked the highest within Harris County.

## Slide 5: Clear Creek, TX Watershed
Notes: This 197 square mile area is situated adjacent to Galveston Bay on the Gulf of Mexico coast and encompasses the four counties of Galveston, Brazoria, Harris, and Fort Bend (Figure 1). The watershed is drained primarily by Clear Creek and associated tributaries.
Out of approximately 31,000 policies purchased, 9,792 made claims during the study period.

## Slide 6
Pattern of Flood Loss

## Slide 7: Flood Loss Descriptive Statistics

## Slide 8: Proximity Results
Ave. claim $34,217
  43% from Hurricane Ike.
55% claims outside floodplain
  Significantly higher for Allison and Ike.
  Ave. distance from boundary 1,378 ft.
  Loss outside significantly lower.
Losses from Ike sign. closer to floodplain
Ave. distance from stream 3,183 ft
  Losses from Ike significantly closer.
Ave. distance from coastline 30,177 ft
  Losses from Ike closer; Allison further inland.

## Slide 10
Notes: Need color version

## Slide 12: Conclusions
100-year floodplain may not be sufficient in predicting actual property damage.
Type of flooding event important in determining the location and extent of significant losses.
Delineating flood risk based on actual loss may better capture/communicate risk.
Dynamic spatial gradient of risk/loss.
Boundaries more responsive to population density, land use, and home value.
Notes: more than half of the insured losses over an eleven-year period occurred outside of the floodplain boundaries most commonly used by local governments and residents to make decisions to mitigate adverse impacts.
surge-based storm adheres more to the boundaries of streams and floodplains. rainfall events can cause flooding in vulnerable areas not necessarily tied to stream segments or traditional floodplains.
Plans and policies should better recognize the patterns of loss stemming from different types of flooding events, rather than take a “once size fits all” approach to flood mitigation.
delineating flood risk based on actual loss (versus simulation or predictive statistical models) may better capture and communicate to decision makers and residents the actuality of property damage occurring from storms.
With this approach, flood risk is not treated dichotomously as a consequence of being either in or out of the floodplain, but risk instead takes the form of a spatial gradient based on actual events. This gradient dissipates further away from the floodplain boundary. Moreover, the location and extent of these gradients is dynamic over time, depending on the type of storm impacting the watershed.

## Slide 13: Next Steps
Refine hotspot mapping procedures.
Explaining flood loss through proximity variables.
Comparing flood loss patterns with 2-D hydrological models for expected flooding.
Extend to other watersheds.
Notes: more than half of the insured losses over an eleven-year period occurred outside of the floodplain boundaries most commonly used by local governments and residents to make decisions to mitigate adverse impacts.
surge-based storm adheres more to the boundaries of streams and floodplains. rainfall events can cause flooding in vulnerable areas not necessarily tied to stream segments or traditional floodplains.
Plans and policies should better recognize the patterns of loss stemming from different types of flooding events, rather than take a “once size fits all” approach to flood mitigation.
delineating flood risk based on actual loss (versus simulation or predictive statistical models) may better capture and communicate to decision makers and residents the actuality of property damage occurring from storms.
With this approach, flood risk is not treated dichotomously as a consequence of being either in or out of the floodplain, but risk instead takes the form of a spatial gradient based on actual events. This gradient dissipates further away from the floodplain boundary. Moreover, the location and extent of these gradients is dynamic over time, depending on the type of storm impacting the watershed.

## Slide 14
Center for Texas Beaches and Shores
Research supported by the National Science Foundation Grant No. CMS- 0346673 & the Houston Endowment