## Slide 1: Gulf Coast Center for Evacuation and Transportation Resiliency
Brian Wolshon, Ph.D., P.E.
and Chester Wilmot, Ph.D., P.E.
Advancements in
Evacuation Planning and Analysis Tools Since
Hurricane Katrina
2012 SSPEED Conference, Rice University April 11, 2012
Brian Wolshon, Ph.D., P.E.
Louisiana State University

## Slide 2: What’s new?
Significant changes in the field of evacuation (fortunately) began several years before Hurricane Katrina… and have continued with other major evacuation events
In general, Hurricane Katrina (and Rita) let us know what we didn’t know – though, arguably, should have
Later evacuations, like those for Hurricanes Gustav and Ike gave an opportunity to use and evaluate new plans, policies, etc.
Many new practices and ideas have been developed to “plan for the last storm”
Gulf Coast Center for Evacuation and Transportation Resiliency

## Slide 3: What’s new?
Leadership at the federal level (USDOT, TRB, NCHRP, etc.), state level (Louisiana, Texas, Florida, etc.), and local level (New Orleans, Houston, etc.)
New evacuation innovations and practices have occurred outside of hurricane hazards
  Wildfires, California
  Nuclear power plant emergencies, NRC
  Terrorist attacks, New York and Washington DC
Research support from NSF, TRB, USDOT, etc.
Gulf Coast Center for Evacuation and Transportation Resiliency

## Slide 4: Significant Areas of Advancement
Evacuation planning for low-mobility and special needs evacuees
Operational enhancements to increase outflow
  Management, infrastructure, control systems
Monitoring and data collection on evacuation routes
Simulation and modeling
  Behavior & decision making -> travel demand estimation -> traffic operation analyses
Testing, drilling, and exercising
Research
Gulf Coast Center for Evacuation and Transportation Resiliency

## Slide 5: Low Mobility and Special Needs
  New awareness and appreciation for this need
  Assisted evacuations using mass transportation resources
  Understanding functional needs; identifying these populations; establishing and maintaining communications with these groups
  Coordination and planning of facility evacuation and sheltering
  Animal-related evacuations (service animals, pets, livestock)
  Improvement through experience and “practice”
Gulf Coast Center for Evacuation and Transportation Resiliency

## Slide 6: Defining “Low Mobility” Evacuees
Individuals without personal transportation, elderly, infirm, tourists, economically disadvantaged, prisoners, homeless, etc.
How many persons fit these description?
Where are they located?
Who are they and what are there needs? medicine, oxygen, dialysis, etc.
Who is responsible for them if they are unable to take of themselves?
Where do they go? How do they come back?
Gulf Coast Center for Evacuation and Transportation Resiliency

## Slide 7
Notes: 7

## Slide 8
Notes: 8
Hazard analysis to identify the area that would need to be evacuated for a particular hazard condition
Vulnerability analysis to ascertain the number of households and people that are susceptible to the threat condition
Behavioral analysis to project how people will respond to the threat
Transportation analysis to assess roadway capacities within the transportation network and identify conditions such as bottlenecks or links vulnerable to the hazard. The objective of the transportation analysis is to develop clearance times within an evacuation area. Clearance times are estimates of the time that would be required to evacuate an area.
Shelter analysis to evaluate the capability of buildings to withstand the hazards conditions and their suitability to be used as refuges for evacuees
Decision making to develop procedures to assess whether a hazard presents a level threat to warrant an evacuation and, if so, when to initiate an evacuation order
Development management to regulate the growth of population and land development that could make evacuation more difficult

## Slide 9
Jefferson Parish Bus Routes
Notes: 9
Hazard analysis to identify the area that would need to be evacuated for a particular hazard condition
Vulnerability analysis to ascertain the number of households and people that are susceptible to the threat condition
Behavioral analysis to project how people will respond to the threat
Transportation analysis to assess roadway capacities within the transportation network and identify conditions such as bottlenecks or links vulnerable to the hazard. The objective of the transportation analysis is to develop clearance times within an evacuation area. Clearance times are estimates of the time that would be required to evacuate an area.
Shelter analysis to evaluate the capability of buildings to withstand the hazards conditions and their suitability to be used as refuges for evacuees
Decision making to develop procedures to assess whether a hazard presents a level threat to warrant an evacuation and, if so, when to initiate an evacuation order
Development management to regulate the growth of population and land development that could make evacuation more difficult

## Slide 11: Operational Enhancements
Transportation system management (TSM) for operational enhancement (capacity)
  Contraflow operations
  Shoulder EVACULANES
  Signals and other control systems
Infrastructure
  “Multipurpose” roadways
  Contraflow gates, crossovers, barriers, shoulders
Control strategies
  Emergency traffic signal control (urban/terrorist threats)
Gulf Coast Center for Evacuation and Transportation Resiliency

## Slide 12
Map Source: LaDOTD
http://www.dotd.state.la.us/maps
Notes: These topics will be addressed from a transportation engineering perspective.
Using examples from recent evacuations in other states and Louisiana.
And showing examples of what were doing at LSU to address some of these issues here and nationally

## Slide 13
Texas EVACULANE Shoulders
US 290
Houston to Hempstead
Notes: These topics will be addressed from a transportation engineering perspective.
Using examples from recent evacuations in other states and Louisiana.
And showing examples of what were doing at LSU to address some of these issues here and nationally

## Slide 14
Texas EVACULANE Shoulders
Notes: These topics will be addressed from a transportation engineering perspective.
Using examples from recent evacuations in other states and Louisiana.
And showing examples of what were doing at LSU to address some of these issues here and nationally

## Slide 15
Variable Message Signs
Notes: These topics will be addressed from a transportation engineering perspective.
Using examples from recent evacuations in other states and Louisiana.
And showing examples of what were doing at LSU to address some of these issues here and nationally

## Slide 16
Contraflow Flip-down Signs
Notes: These topics will be addressed from a transportation engineering perspective.
Using examples from recent evacuations in other states and Louisiana.
And showing examples of what were doing at LSU to address some of these issues here and nationally

## Slide 17
Go Trailers
Notes: These topics will be addressed from a transportation engineering perspective.
Using examples from recent evacuations in other states and Louisiana.
And showing examples of what were doing at LSU to address some of these issues here and nationally

## Slide 18: Monitoring and Data Collection
Application, adaptation of, and integration with legacy systems
Real-time situational awareness
We can now see how evacuations progress temporally and spatially
Data sets for:
  Review of processes
  Analysis of flow conditions
  Verification, validation, and calibration of models
Gulf Coast Center for Evacuation and Transportation Resiliency

## Slide 19
Westbound (outbound) Lanes – LaPlace, Louisiana
0
500
1000
1500
2000
2500
3000
0
12
24
12
24
12
24
12
24
12
24
THURSDAY FRIDAY SATURDAY SUNDAY MONDAY
Ave. of Prior
3 Weeks
Katrina
Evacuation
Storm Landfall
Duration of Evacuation Volume
(Data source: LA DOTD)

## Slide 20
0
500
1000
1500
2000
2500
3000
3500
4000
4500
5000
0
12
24
12
24
12
24
12
24
12
24
12
24
12
24
TUESDAY WEDNESDAY FRIDAY SATURDAY SUNDAY MONDAY
Hurricane Ivan
9/14 and 9/15, 2004
Hurricane Katrina
8/26 thru 8/29, 2005
Total
Northbound
Volume
w/ contraflow
Northbound Volume
in “Normal” Lanes
Total
Northbound
Volume
Contraflow Performance
(Data source: LA DOTD)

## Slide 21
Gulf Coast Center for Evacuation and Transportation Resiliency
Notes: Hazard analysis to identify the area that would need to be evacuated for a particular hazard condition
Vulnerability analysis to ascertain the number of households and people that are susceptible to the threat condition
Behavioral analysis to project how people will respond to the threat
Transportation analysis to assess roadway capacities within the transportation network and identify conditions such as bottlenecks or links vulnerable to the hazard. The objective of the transportation analysis is to develop clearance times within an evacuation area. Clearance times are estimates of the time that would be required to evacuate an area.
Shelter analysis to evaluate the capability of buildings to withstand the hazards conditions and their suitability to be used as refuges for evacuees
Decision making to develop procedures to assess whether a hazard presents a level threat to warrant an evacuation and, if so, when to initiate an evacuation order
Development management to regulate the growth of population and land development that could make evacuation more difficult

## Slide 22: Simulation and Modeling
Evacuee behavior and response to threats
Travel demand forecasting
Traffic operational analysis
Process optimization
Scenario development and evaluation
Multimodal evacuation processes
Research -> MegaRegion analysis
Gulf Coast Center for Evacuation and Transportation Resiliency

## Slide 23: Evacuation Traffic Simulation
Has proven value and acceptance in the field
Permits bottlenecks to be identified and potential solutions to be analyzed before they become problems
Gives quantitative MOE results to decision-makers
Allows effects of alternative strategies and adverse conditions to be assessed without consequence
Gulf Coast Center for Evacuation and Transportation Resiliency

## Slide 24
Behavioral Modeling
Forecast time-dependent evacuation demand
Chart: 2-hour time intervals
| interval 1 | interval 2 | interval 3 | interval 4 | interval 5 | interval 6 | interval 7 | interval 8 | interval 9 | interval 10 | interval 11 | interval 12 | interval 13 | interval 14 | interval 15 | interval 16 | interval 17 | interval 18 | interval 19 | interval 20 | interval 21 | interval 22 | interval 23 | interval 24 | interval 25 | interval 26 | interval 27 | interval 28 | interval 29 | interval 30 | interval 31 | interval 32 | interval 33 | interval 34 | interval 35 | interval 36 | interval 37 | interval 38 | interval 39 | interval 40 | interval 41 | interval 42 | interval 43 | interval 44 | interval 45 | interval 46 | interval 47 | interval 48
Observed | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 3 | 1 | 0 | 0 | 0 | 0 | 1 | 2 | 1 | 2 | 0 | 2 | 3 | 2 | 1 | 0 | 1 | 0 | 0 | 2 | 4 | 12 | 29 | 35 | 25 | 26 | 11 | 6 | 2 | 1 | 2 | 4 | 12 | 14 | 15 | 10 | 6 | 3 | 3 | 1 | 1
Predicted | 0.1415 | 0.14171 | 0.14321 | 0.57917 | 0.61038 | 1.4505 | 1.5055 | 1.6139 | 0.93251 | 1.1322 | 0.27135 | 0.27451 | 0.30027 | 0.33585 | 0.33986 | 1.3468 | 1.3894 | 3.3798 | 3.4495 | 3.4714 | 1.9936 | 2.021 | 0.42737 | 0.44164 | 0.47502 | 0.50677 | 0.5342 | 13.7033 | 12.7698 | 27.9674 | 32.5701 | 29.426 | 16.132 | 15.7554 | 3.1433 | 3.08 | 2.9022 | 2.7662 | 2.356 | 7.9913 | 6.4441 | 11.3165 | 9.1812 | 7.0367 | 3.2652 | 2.8957 | 0.5598 | 0.55543
Notes: Sequential logit model developed which predicts whether a household will evacuate and when it will do so.
Prob (hh evacuates in time period t) is function of:
  distance of storm from household in each time interval
  forward speed of the hurricane in each time interval
  flooding potential of home
  whether the home is a mobile home or not
  evacuation orders in effect in each time interval.

## Slide 25
Regional-Level Modeling and Visualization

## Slide 26
Station 42
Station15
Station 27
Station
54
Station
88
Station
67
Station18
I -12
I -12
I -10
US-61
I -10
I -10
US-61
I -10
I -10
I -55
I -59
I -55
Lake Pontchartrian
Causeway
New
Orleans
Baton
Rouge
Hammond
North to Mississippi
North
Map Source: LaDOTD
http://www.dotd.state.la.us/maps
Notes: These topics will be addressed from a transportation engineering perspective.
Using examples from recent evacuations in other states and Louisiana.
And showing examples of what were doing at LSU to address some of these issues here and nationally

## Slide 27
LaPlace Data Station
10:00am - Sunday
Baton Rouge
New Orleans
Westbound I-10 Traffic Speed

## Slide 28
Scenario Testing and Evaluation
Analysis of “variable” hazards and responses
Temporal –
  More/less time to evacuate
  implementation of phasing strategies
  Spatial –
    Storm size and direction of approach
    network management
Notes: Sequential logit model developed which predicts whether a household will evacuate and when it will do so.
Prob (hh evacuates in time period t) is function of:
  distance of storm from household in each time interval
  forward speed of the hurricane in each time interval
  flooding potential of home
  whether the home is a mobile home or not
  evacuation orders in effect in each time interval.

## Slide 29
Future Modeling
  Police enforcement control
  MegaRegion evacuation network analysis
Beaumont
Port Arthur
Lake
Charles
Lafayette
Baton
Rouge
New
Orleans
N
Houston