## Slide 1
Jude A. Benavides, Ph.D.
Department of Chemistry and
Environmental Sciences
The University of Texas at Brownsville
April 11th, 2012
Hurricane Threat and Flood Mitigation
In South Texas

## Slide 2: Lower Rio Grande Valley
Lower Rio Grande Valley (LRGV)
  Population (2010): 1.3 Million
  Population (2020 est): 1.78 Million
Including Matamoros and Reynosa, Mexico
  Pop (2010): 2.1 Million
  Pop (2020): ~ 2.7 Million

## Slide 3: The Rio Grande Watershed and the LRGV

## Slide 5: Lower Rio Grande River Flood Control Project (Dams, Diversion / by-pass channels, levees)
250,000 cubic feet per second (cfs) at Rio Grande City (inflow to Anzalduas Dam);
105,000 cfs for diversion by Anzalduas to the U.S. floodway (Main floodway)
105,000 cfs for diversion by Retamal to the Mexican floodway
84,000 cfs in the North Floodway (diverted from the Arroyo Colorado)
21,000 cfs in the Arroyo Colorado at Harlingen
20,000 cfs in the Rio Grande at Brownsville / Matamoros.

## Slide 6: Houston and South Texas
Rainfall
  50-60% of Houston area annual rainfall
  22 – 28 inches
100-yr 24-hour storm
  11.7 inches vice 13.5 inches
Drier climate (semi-arid to sub-tropical)
  Periodic, intense rainfall
  Often tropical

## Slide 7
Hurricane Strike Counts by County

## Slide 9
Keim et al., 2007

## Slide 10
Chart: Return Period for Tropical Storms and Hurricanes Along U.S. Gulf of Mexico and Atlantic Coast
TS and Hurricanes | 5 | 5 | 4 | 3 | 3 | 3 | 3 | 4 | 3 | 3 | 3 | 4 | 4 | 4 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 5 | 4 | 3 | 4 | 3 | 2 | 2 | 3 | 4 | 6 | 10 | 10 | 6 | 8 | 9 | 7 | 12 | 12 | 12 | 10
< ------ Gulf of Mexico ------ >
< -- S. Atlantic Coast -- >
< - N. Atlantic Coast - >
Brownsville, TX
Galveston, TX
New Orleans, LA
Mobile, AL
Panama City, FL
St. Petersburg, FL
Miami, FL
Cocoa Beach, FL
Jacksonville, FL
Charleston, SC
Cape
Hatteras,
NC
Virginia
Beach, VA
Atlantic City, NJ
Newport, RI
Eastport, ME
Keim et al., 2007

## Slide 12: b
NOAA Coastal Services Center
Online Historical Data Tracker
www.csc.noaa.gov/hurricanes

## Slide 18
Amistad Dam
Falcon Dam
Marte R. Gomez Dam

## Slide 19: Lower Rio Grande River Flood Control Project (Dams, Diversion / by-pass channels, levees)
250,000 cubic feet per second (cfs) at Rio Grande City (inflow to Anzalduas Dam);
105,000 cfs for diversion by Anzalduas to the U.S. floodway (Main floodway)
105,000 cfs for diversion by Retamal to the Mexican floodway
84,000 cfs in the North Floodway (diverted from the Arroyo Colorado)
21,000 cfs in the Arroyo Colorado at Harlingen
20,000 cfs in the Rio Grande at Brownsville / Matamoros.

## Slide 20: Lower Rio Grande River Flood Control Project (Dams, Diversion / by-pass channels, levees)
250,000 cubic feet per second (cfs) at Rio Grande City (inflow to Anzalduas Dam);
105,000 cfs for diversion by Anzalduas to the U.S. floodway (Main floodway)
105,000 cfs for diversion by Retamal to the Mexican floodway
84,000 cfs in the North Floodway (diverted from the Arroyo Colorado)
21,000 cfs in the Arroyo Colorado at Harlingen
20,000 cfs in the Rio Grande at Brownsville / Matamoros.

## Slide 21: Structural “Flood Control” System Severely Tested
Limited conveyance due to poor channel maintenance
Levee erosion – wind, vehicular traffic, rain, settling
System was limited to 50-70% of design conveyance in some areas
Local rainfall runoff had to be stored due to floodways being activated

## Slide 22: Opportunity for SSPEED
Enhanced flood modeling and analysis of real-world conveyance capacity
Incorporation of non-structural methods
  Flood Alert systems
  De-coupling of the LRGFCP and local runoff
Evacuation studies
Storm Surge and Runoff Analysis
Education and Outreach!!
Collaborative research through REU’s and thesis opportunities

## Slide 23
Work to date:
  Flood models
    LIDAR, GIS
    Assessment for gaging needs for calibration
  Water Quality / TMDL Modeling
  University cooperatives
    UTB/TSC, Rice, TAMUK,
    SSPEED Center
  On-going efforts at US Army Corps dredging operations
Work funded in part by Texas Water
Development Board
Detailed Floodplain and Flood Damage Reduction Alternatives Analysis Completed  master planning, stormwater management and emergency preparedness

## Slide 25
Work funded in part by City of Brownsville
and the Kleberg Foundation
University students collecting much needed data including: bathymetry, sedimentation rates, water quality index establishment, target goal establishment, etc.
Work to date:
  Flood models
    LIDAR, GIS
    Assessment for gaging needs for calibration
  Water Quality / TMDL Modeling
  University cooperatives
    UTB/TSC, Rice, TAMUK,
    SSPEED Center
  On-going efforts at US Army Corps dredging operations

## Slide 27
Work to date:
  Flood models
    LIDAR, GIS
    Assessment for gaging needs for calibration
  Water Quality / TMDL Modeling
  University cooperatives
    UTB/TSC, Rice, TAMUK,
    SSPEED Center
  On-going efforts at US Army Corps dredging operations

## Slide 28: Dredging Process
Estimated Removal of Approximately 100,000 cubic yards in 4 Pilot Sites

## Slide 29: What Happens to Dredged Material?
Dredged Sediment Slurry
Sent to Dewatering System
Clean Water
Back to Resacas
Dry Sediment
Loaded
& Hauled
Landfill
Fill Material
Other Options?

## Slide 30
Questions?????