## Slide 1: Calibration A Hands-On Approach to Making a Model Reflect Reality
Andy Yung, P.E., CFM
DODSON | a Walter P Moore Company

## Slide 2: Lessons from my grandfather…

## Slide 3: Purpose of Models
Focus on HEC-HMS & HEC-RAS
Uses of Models:
  Planning & Design of Flood Reduction Facilities
  Operating and/or Evaluating Existing Hydraulic-Conveyance Facilities
  Preparing for and Responding to Floods
  Regulating Floodplain Activities
Goals of Accurate Modeling:
  To reduce damages
  To save lives

## Slide 4: The Problem…
How do we make these…

## Slide 5: The Problem…
…match this with any degree of accuracy?

## Slide 6: The Problem…
Too often, our model results look like this…

## Slide 7: The Problem…
Or this…

## Slide 8: Method of Calibration
Adjust “n” Values in HEC-RAS to Fit USGS Rating Data
Modify “Observed” Hydrographs Based on New HEC-RAS Rating Curve
Perform Calibration of Loss Rates
Develop Station vs. Discharge Relationship for Multi-Frequency Flow File
Review Available Data
Compare Calibration Results to Observed Hydrographs, Peak Qs, and HWMs
Final Review of Analysis with Available Data
Compare Frequency Results to FFA and Effective BFEs
Review Next
Downstream Gage
Check Historical Storm Analysis vs. Observed Data
Check Frequency Flows vs. Flood Frequency Analysis

## Slide 9: Start with the “Knowns”
The problem really lies with the unknowns. Therefore, we have to start any calibration with what we do know.
The things we can actually measure…
  Hydrology: rainfall, drainage areas, observed hydrographs, reservoir capacity
  Hydraulics: rating curve information, high water marks, cross section geometry, bridge structures

## Slide 10: The Biggest “Unknowns”
Manning’s “n” Values
  Affects water surface calculations
  Affects river routing (storage in floodplain)
Loss Rates
  Affects volume of runoff
  Affects peak discharges
Other lesser known unknowns…
  Ineffective flow areas
  Bridge modeling routines
  Timing

## Slide 11: Method of Calibration
Adjust “n” Values in HEC-RAS to Fit USGS Rating Data
Modify “Observed” Hydrographs Based on New HEC-RAS Rating Curve
Perform Calibration of Loss Rates
Develop Station vs. Discharge Relationship for Multi-Frequency Flow File
Review Available Data
Compare Calibration Results to Observed Hydrographs, Peak Qs, and HWMs
Final Review of Analysis with Available Data
Compare Frequency Results to FFA and Effective BFEs
Review Next
Downstream Gage
Check Historical Storm Analysis vs. Observed Data
Check Frequency Flows vs. Flood Frequency Analysis

## Slide 12: Manning’s “n” Value
“In applying the Manning formula…the greatest difficulty lies in the determination of the roughness coefficient n; for there is no exact method of selecting the n value. At the present stage of knowledge, to select a value of n actually means to estimate the resistance to flow in a given channel, which is really a matter of intangibles. To veteran engineers, this means the exercise of sound engineering judgment and experience; for beginners, it can be no more than a guess, and different individuals will obtain different results.”
--V.T. Chow, Open-Channel Hydraulics

## Slide 13: Manning’s “n” Value
n = 0.026 (USBR)
n = 0.040 (Chow)

## Slide 14: Rating Curves (steady flow)
Notes: test

## Slide 15: Rating Curves (unsteady flow)
Notes: test

## Slide 16: Loss Rates
Highly dependent upon the type of soil, land use, and the amount of antecedent saturation prior to the storm event

## Slide 17: Other Items Affecting Calibration
No substitute for field investigation

## Slide 18: Method of Calibration
Adjust “n” Values in HEC-RAS to Fit USGS Rating Data
Modify “Observed” Hydrographs Based on New HEC-RAS Rating Curve
Perform Calibration of Loss Rates
Develop Station vs. Discharge Relationship for Multi-Frequency Flow File
Review Available Data
Compare Calibration Results to Observed Hydrographs, Peak Qs, and HWMs
Final Review of Analysis with Available Data
Compare Frequency Results to FFA and Effective BFEs
Review Next
Downstream Gage
Check Historical Storm Analysis vs. Observed Data
Check Frequency Flows vs. Flood Frequency Analysis

## Slide 19: Numerical Goals for Calibration
Flows (compared to USGS observations)
  Good = Less than 10%
  Fair = 10% to 20%
  Poor = More than 20%
Elevations
  Good = Less than 1.0 foot
  Fair = 1.0 to 3.0 feet
  Poor = 3.0 feet

## Slide 20: High Water Mark Comparisons

## Slide 21: Hydrographs & Profiles

## Slide 22: Method of Calibration
Adjust “n” Values in HEC-RAS to Fit USGS Rating Data
Modify “Observed” Hydrographs Based on New HEC-RAS Rating Curve
Perform Calibration of Loss Rates
Develop Station vs. Discharge Relationship for Multi-Frequency Flow File
Review Available Data
Compare Calibration Results to Observed Hydrographs, Peak Qs, and HWMs
Final Review of Analysis with Available Data
Compare Frequency Results to FFA and Effective BFEs
Review Next
Downstream Gage
Check Historical Storm Analysis vs. Observed Data
Check Frequency Flows vs. Flood Frequency Analysis

## Slide 23: Flood Frequency Analyses

## Slide 24: Lessons from my son…
Keep it “SimpleMan”
  Think logically about reasons why the model doesn’t fit reality
  Remember that calibration usually boils down to a few simple unknowns
  Get out in the field and see what you can find (models are tools, not black boxes with all the answers)

## Slide 25
Questions?