## Slide 1: The Human Element in hydrologic and hydraulic Modeling
Consideration of
Duane Barrett, P.E., CFM
HDR Engineering, Inc.

## Slide 2: WHAT’S “modelING?”
Modeling involves an effort to represent a large, complex system on a smaller scale or through the use of only a sampling of data as opposed to a complete accounting of the physical system. In the context of hydrologic and hydraulic studies, models are used to analyze or predict the responses of water- sheds or drainage systems to rainfall events.

## Slide 3: Why Model?
Models make it possible to analyze very complex drainage systems quickly and efficiently.
Computer models allow users to establish baseline watershed/hydraulic conditions, evaluate changes to a watershed or a drainage system, analyze different storm events, assess system sensitivity, etc.

## Slide 4: Steps In model development & use
Problem Definition
Site Investigation
Data Collection
Site/Watershed Characterization
Model Construction
Model Calibration
Model Utilization

## Slide 5: EXTERNAL INFLUENCES
Model development is often influenced by the following factors, which are not directly related to the watershed or system being analyzed.
Software
Hardware
Standard Practice
Drainage Criteria
Standardization

## Slide 6: Modeler-Supplied influences
One of the biggest influences on the modeling process is the modeler, and his or her performance may be affected by a number of factors.
Ability
Experience
Creativity
Knowledge
as well as …
Work Load
Distractions
Level of Interest
Quality of Oversight

## Slide 7: THE HUMAN ELEMENT IN MODELING
SoftwareCapability
Human Input
Rules & Criteria
HYDROLOGY & HYDRAULICS GUIDANCE MANUAL

## Slide 8: HOW reliable are MODELS?
To what extent should decision makers rely on models?
Models may be very reliable if the underlying work is good and the application is appropriate. However, the decision maker must understand the model’s purposes and limitations.
IS THIS SOFTWARE APPLICABLE TO THE PROBLEM?

## Slide 9: Accuracy versus reliability
“Accuracy” is a frequently misused term when applied to models.
Use of the term “accuracy” implies that there is a known result, but this is not normally the case.
Models may be “reliable” or “reasonable,” but not really “accurate!”
On the other hand, precision is absolutely attainable with computer models.

## Slide 10: Teaming Humans and computers
Humans are good at …
Computers are good at …
CREATIVITY
SUBTLETY
PROBLEM-SOLVING
COMPLEXITY
DREAMING
SPEED
COMPLEX CALCULATIONS
PRECISION
REPRODUCIBILITY
FOLLOWING INSTRUCTIONS
The combined talents and capabilities of humans and computers yield wonderful things in terms of hydrologic and hydraulic modeling!

## Slide 11: Humans good, humans bad
It is ironic that the things that make human involvement indispensable to the modeling process also make the process somewhat unpredictable. To combat this, software designers have provided for much higher levels of automation.
♫
♪
♫
♪

## Slide 12: How about automation?
Powerful Computers
Improved Software
Comprehensive Data
  LiDAR
  Weather Radar
  Gaging Systems
“Just pour in the data, and
let “Deep Blue" do the work.”
EASY
LIDAR
GAGES
RAINFALL
NO MORE LIABILITY!

## Slide 13: MODEL & DATA SOPHISTICATION have INCREASEd tremendously
HEC-1
HEC-2
WSP-2
TR-20
HEC-HMS
HEC-RAS
SWMM
INFOWORKS
+
LIDAR, NEXRAD, RECORDING GAGES …

## Slide 14: But are we ready for this?
Change that roughness coefficient to 0.035, please, Hal.
I’M SORRY, DAVE. I‘M AFRAID I CAN’T DO THAT.

## Slide 15: Case study: TSARP/brays bayou (2002)
LiDAR + PrePRO (HEC-GeoHMS)
Automated Drainage Boundary Delineation
Surface vs. Underground Drainage
Engineering Judgment Required to Resolve Boundaries
Surface Drainage
Storm Sewers

## Slide 16: Case study: SWMM OUTPUT
Model results may show losses of storm runoff if storage areas are not carefully defined.
Computed hydraulic grade line elevations may exceed natural ground elevations significantly.
Error messages may not reveal these problems without careful QA/QC!

## Slide 17: So in summary …
Full automation is not possible. (No HAL 9000 computers available as of 2012.)
Humans have perhaps too much personality and are frequently affected by circumstances unrelated to the development and utilization of modeling products
On the other hand, computers and software lack the imagination and creativity frequently needed to develop the best and most reliable models.

## Slide 18: Where does this leave the decision maker?
Can hydrologic and hydraulic models be trusted for critical decision making?
Absolutely! The combination of human ingenuity and powerful modeling tools provide extremely powerful and reliable tools for decision making. However, the decision maker should ask a few questions about models created for any given purpose.

## Slide 19: Questions for decision makers
What is the problem?
What is the modeling software designed to do?
How does the software work?
Are the problem & software properly matched?
What purpose is the model intended to fulfill?
Has the model been calibrated and how well?
Has the model been through a good QA/QC process?
What are the consequences of an error of a given magnitude?
Are the results reasonable/reliable?
If you don’t know these answers, ask the engineer and/or the modeler. They should know!

## Slide 20: “THERE’S SOME ART IN THERE”
Lynn Lovell, Halff Associates, Inc.
April 4, 2012
Draft Model
Vincent Van Gogh
Well-Calibrated Model
Jan Vermeer
Trouble!
Pablo Picasso

## Slide 21: Questions for the presenter?
If I can’t answer your question in 30 seconds, I’ll just move on to the next one. Hey, we’re on a schedule here.
answer