## Slide 1: “Why elevation is our salvation from inundation”
Roy K. Dokka, Ph.D.
Center for GeoInformatics and
Louisiana Spatial Reference Center
Louisiana State University,
Baton Rouge, LA 70803
Louisiana
State
University

## Slide 2: This is what I’m talkin’ ‘bout!
Coastal engineering design, hazard mitigation, planning, depend on accurate land elevation and bathymetry.
Subsidence has destroyed vertical control from Pensacola to Corpus Christi.
The lack of vertical control has lead to compromised LiDAR, leading to unrealistic surge models, FEMA flood maps that do not accurately portray risk, misguided coastal planning policy, and ultimately to an unsustainable coast.
Although we have solved the technical issues regarding control in Louisiana, there is little understanding by officials, professionals or the public regarding the problem and implications.

## Slide 3: What is vertical control?
Most simply put, a point of vertical reference, a known point. A mental construct.
Practical manifestation: National Spatial Reference System. Maintained by NGS/NOAA and others. National datums like NAVD 88.
Typically accessed via passive (benchmarks) and active (CORS) access points.
Sea level? Different issue.

## Slide 4: The Problem(s)
The Earth is dynamic.
As the Earth moves, so can the benchmarks and CORS.
Datums do not change.
How much is too much?
Benchmarks are only known for the date they are calibrated. CORS can be tracked spatially through time.
Because calibration is very expensive, most benchmarks in Texas and Louisiana have gone stale.
Over time, the benchmarks may move several feet with respect to the datum.

## Slide 5
NOAA told the U.S. Congress in 2001 that the system used to measure elevations in LA was,
Local vertical control for LiDAR, Flood Mapping, and NFIP Certificates
“inaccurate and
obsolete and unable to
support public safety.”
Accurate elevations were not restored until late 2005. Any elevations obtained between 2001 and 2005 are highly suspect. That is when LiDAR was collected.

## Slide 6: A system of accurate elevations has been impossible to maintain in LA
Why?
Subsidence.
A lack of understanding of how and why subsidence occurs.
A willingness to accept “the best available data” instead of “accurate and sufficiently precise data to meet requirements and the standard of care”.
No Leadership or $$

## Slide 7
Green square
-1/2 inch/yr
Stars
0 inch/yr
uplift
stable
Coastal parishes
avg. = ~-1/2 inch/yr
Yellow circle
-3/4 inch/yr
Blue square
-1/3 inch/yr
Geodetic leveling
shows that vertical
motions vary in
time and space
Shinkle and Dokka (2004)
NOAA Tech. Rept. 50
1960s-1980s

## Slide 8
Benchmarks of Texas and Louisiana—
Before and after Katrina

## Slide 9
GULFNet RTN
Error is 1 cm Horiz.
2cm Vert.,
EVERYWHERE!

## Slide 10
RTN Real-Time Network
Based on VRS technology
“Positioning anywhere,
any time”
Cellular device to
connect user to
Internet and LSU
GULFNet RTN
Kinematic mode:
+ 0.3 ft (1 sec.)
Relative vertical:
+ 2 cm (3 min.)
Native output in “CORS 2002” but can easily
be put in 2004.65 context through calibration.

## Slide 11: ADCIRC models need real weir elevations to be realistic
FEMA says this is
where the levee is
and how high it is.
Here is where it really
is and what its actual
height is.
FEMA is off by 16 feet!!

## Slide 12
Flood maps did not capture important details needed for modeling in Cameron

## Slide 13
Bottom Line:
Cameron Parish is higher and more “rough” than FEMA thought. Result: an adjustment of flood maps.

## Slide 14
NGS data
Analysis of Geodetic Leveling
Southeast Texas 1918-1987
K. Shinkle, 2005

## Slide 16
Beaumont, TX
I-10 at US 90
  FEMA weirs (green)
Gulfnet RTN (black)
US 90

## Slide 17: Take-aways
Coastal engineering design, hazard mitigation, planning, depend on accurate land elevation and bathymetry.
Subsidence has destroyed vertical control from Pensacola to Corpus Christi.
The lack of vertical control has lead to compromised LiDAR, leading to unrealistic surge models, FEMA flood maps that do not accurately portray risk, misguided coastal planning policy, and ultimately to an unsustainable coast.
Although we have solved the technical issues regarding control in Louisiana, there is little understanding by officials, professionals or the public regarding the problem and implications.

## Slide 18
Thank You!

## Slide 19: Enforcement of QA/QC standards for LiDAR Data—Sampling
FEMA needs to insist that mapping partners
follow requirements set forth in:
“Guidelines and Specifications
For Flood Hazard Mapping
Partners”

## Slide 20: Improvement of QA/QC standards for LiDAR Data— Sampling Distribution
FEMA needs to insist that test samples for QA/QC
be random and well distributed though out the
test area.
The samples in TA05,
are obviously not
representative of the
area.
This is the case
for all LA LiDAR
QA/QC.

## Slide 21
A.8.6.2 Ground Cover Categories [February 2002]
The assigned Mapping Partner shall separately evaluate and
report on the TIN accuracy for the main categories of ground
cover in the study area, including the following:
1. Bare-earth and low grass (e.g., plowed fields, lawns, golf courses);
2. High grass, weeds, and crops (e.g., hay fields, corn fields, wheat fields);
3. Brush lands and low trees (e.g., chaparrals, mesquite);
4. Forested, fully covered by trees (e.g., hardwoods, evergreens, mixed
forests);
5. Urban areas (e.g., high, dense manmade structures);
6. Sawgrass; and
7. Mangrove.
On page A-46

## Slide 22
“The assigned Mapping Partner shall select a
minimum of 20 test points for each major
vegetation category identified. Therefore, a
minimum of 60 test points shall be selected for
three (minimum) major land cover categories,
80 test points for four major categories, and so
on.”
Also on page A-46

## Slide 23
Every category must have 20 samples
Unfortunately, QA/QC was
not done properly in ANY
parish in LA!
One of the last
Claiborne Parish
2008
One of the first
Plaquemines,
Jefferson, and
Lafourche Parishes
2008

## Slide 24: FEMA needs to require scientific handling of statistical outliers
Scientific and surveying practice does not recognize
arbitrary removal of data without cause, i.e., are the
errors really outliers or are they representative.
FEMA allows for removal of statistical outliers. FEMA
Guidelines recognize that, "Statisticians almost
unanimously agree that errors exceeding the
"3-sigma" level are outliers.” That is 0.25% of a
dataset.
Statistical outliers associated with LA lidar were
removed without explanation. FEMA allowed as much
as 10% of the data to be removed without cause.
Data that would have failed the QA test wound up
passing.

## Slide 25: Storm Surge Modeling and Topography
The flow of surge in coastal Louisiana is largely controlled by:
 natural ridges
 levees, walls, sheetpiles.
 roadways, railroad beds.
Thus, one of the key inputs for storm surge models is topography.
The Problem: Given that subsidence has lowered the land surface and ruined the vertical control network we use to reference elevations, how reliable are storm surge models?

## Slide 27: Local biologists show that plants are larger and offer more storm surge protection

## Slide 28: The Public expects FEMA to use accurate and up-to-date data in its creation of DFIRMs
The actual standard is the doctrine
of the:
“Best available”
Consider the example of bathymetry used in storm surge modeling

## Slide 29
Bathymetric Maps of LA are Ancient!

## Slide 31
FEMA’s
Model
ADCIRC model for Rita in
Cameron Parish can be improved
by raising topography and
increasing friction.
Sensitivity Test—
Lower topography
and/or less friction
Sensitivity Test—
Higher topography
and/or more friction

## Slide 32: What is the overall strategy regarding 3-D positioning in LA?
The ability to obtain accurate elevations has always been a shared responsibility between NGS, local government, surveyors, and others.
NGS is committed to providing users in LA with access to the NSRS. This means maintaining a basic backbone of about a hundred benchmarks in south Louisiana, supporting CORS, development of technical standards.
C4G will provide state-wide GNSS technology to facilitate accurate and precise “anywhere-any time” 3-D positioning.
Local people will have to decide how they wish to access the NSRS. NGS and C4G are dedicated to helping individual parishes craft viable local solutions to meet local needs and $$ issues.

## Slide 33: LSU’s Role in Fixing the Problem
Operation of GULFNet GPS Reference Network across South Louisiana
42 CORS. Users can access the National Spatial Reference System anywhere in Louisiana with confidence. Think of CORS as “smart benchmarks”. GULFNet is updated daily and will remain accurate into the future without costly re-observations. Heights recognized as legal under Louisiana State law. www.ngs.noaa/CORS
Creation of a State-wide Real-time Network
GULFNet real-time kinematic GPS RTN network allows users to obtain accurate and precise 3-D positions anywhere-anytime in Louisiana. Precision: 1 cm Horiz., 2 cm Vert. Users can obtain 2004.65 elevations by site calibration.
Training
Provide know-how to enable users to exploit the new resources.
“Positioning Louisiana for the future”

## Slide 34
The Louisiana Legislature requested LSU
measure the height of the South LA HPS
in 2006-2007. N = 50,000 points
Note: Does not reflect
post 2007 changes
Due to construction by
USACE

## Slide 35
IHNC-MRGO Floodwalls and Levees

## Slide 36
Operational
NHC Katrina
SLOSH model
using outdated
or assumed
elevation data
Katrina SLOSH
using accurate
topography
Note: The so-called “funnel” is
a modeling artifact caused by the use of authorizied elevations
instead of valid measurements
along south levee of MRGO.

## Slide 37
ADCIRC Model Used by
Engineers and Scientists to Plan for
Future Hurricane Storm Surge Also
Shows This Modeling Artifact
Major underestimation
of the height of
Katrina storm surge
in St. Bernard Parish
Conclusion:
MRGO “funnel effect”
is an artifact of modeling
using inaccurate elevations

## Slide 38: Conclusions
New FEMA flood maps are here and more are coming. They are an improvement over the past.
The DFIRM program is founded on IMPROVEMENT.
Begin with a spirit of constructive engagement.
Recognize the difficulty and scope of the job FEMA has undertaken.
Recognize that community partners can often bring technical insights, experience, and attention to detail that “outsiders” cannot match.

## Slide 39: Improvements
More effective education regarding the responsibilities of all parties participating in the NFIP.
Increase the time period for protests.
Recognize that there are problems with data.
Greater adherence to FEMAs guidelines by mapping partners in the preparation of DFIRMs.
Seek improvement and validation of flooding and wave models used by FEMA mapping partners to help establish risks.
Educate communities regarding responsibility their responsibility to maintain vertical control.
The State of Louisiana should follow the North Carolina-FEMA partnership model.

## Slide 40: Storm surge models used to establish risk are unreliable
The model would be reliable
if 99% of blue dots occurred
between the red lines.

## Slide 41: The “Best Available” is a concept of expediency. It is totally inadequate when lives and property are at stake.