## Slide 1
Hurricane Ike Revisited:
What We’ve Learned – Questions Remaining
Carol A. Lewis, Ph.D.
Associate Professor and Director
September 14, 2009
CTTR
Texas Southern University

## Slide 2: Planning for Hurricane Events in Southeast Texas
Pre-Rita
  ▫ Texas DPS Plan (Designated Routes & Control Points)
  ▫ TxDOT Signed Evacuation Routes & Responded
Post-Rita
  ▫ Governor’s Task Force Spurred Changes:
    Command, Control, Communication
    ▫ Evacuation of Special Needs
    ▫ Fuel Availability
    ▫ Flow of Traffic
    ▫ Public Awareness

## Slide 3: Considerations for Elected Officials During a Hurricane Threat
Command, Control and Communication
Evacuation of People with Special Needs
Fuel Availability
Flow of Traffic
Public Awareness

## Slide 4: Command, Control, Communication

## Slide 5: Messages From Elected Officials
● Best Way to Avoid Evacuation Congestion is to Follow the Zonal Plan
● Monitor and Coordinate Messages to Ensure Simultaneous Information to Constituents
Non-essential tripmaking was discouraged beginning
noon on September 11

## Slide 6: Areas of Emphasis
• Identify bottlenecks
• Assess effectiveness of alternative traffic
control strategies
• Assess the effectiveness of different
evacuation strategies

## Slide 7: Considerations for Elected Officials During a Hurricane Threat
Command, Control and Communication
Evacuation of People with Special Needs
Fuel Availability
Flow of Traffic
Public Awareness

## Slide 10: Considerations for Elected Officials During a Hurricane Threat
Command, Control and Communication
Evacuation of People with Special Needsacuation of People with Special Needs
Fuel Availability
Flow of Traffic
Public Awareness

## Slide 11: Fuel Availability
Vehicles to refuel stations were standing by as were arrangements to fuel anyone who ran out of gas in route.

## Slide 12: Considerations for Elected Officials During a Hurricane Threat
Command, Control and Communication
Evacuation of People with Special Needsacuation of People with Special Needs
Fuel Availability
Flow of Traffic
Public Awareness

## Slide 13
Evacuation Plan

## Slide 14: From Literature
Traveler behavior difficult to predict (Peacock et. al.,2007; Murray-Tuite and Mahmassani, January 2005)

## Slide 15: If you evacuated, when did you leave? (422 responses)
Notes: In terms of when the evacuees departed; 60% left either before or during the voluntary evacuation time period, while the remaining 40% departed after the mandatory evacuation orders were given. This is important in that the more spread out the evacuation traffic is on the roadways, any developing congestion may be lessened.

## Slide 16: Traffic Volumes Rita and Ike
Hours into Evacuation | Rita Average Weekday | Rita % of Average Weekday (9/21 and 9/22) | Ike Average Weekday | Ike % of Average Weekday (9/11 and 9/12)
5 | 1667 | .76 | 2963 | .84
10 | 4613 | .60 | 5314 | .96
15 | 5403 | .81 | 6097 | .65
20 | 3445 | .77 | 4428 | .56
Total (All Hours) | 87,995 | . 73 | 102,740 | .72
I-45 (NB) and Beltway 8
I-45 (NB) and Airline

## Slide 17: Contra-Flow Plan

## Slide 18: Considerations for Elected Officials During a Hurricane Threat
Command, Control and Communication
Evacuation of People with Special Needsacuation of People with Special Needs
Fuel Availability
Flow of Traffic
Public Awareness

## Slide 19: Public Awareness
During Hurricane Rita, most
residents made decisions:
▫ Friends and relatives (Peacock
et. al, 2007).
▫ 20% friends and relatives per
TranStar
During Hurricane Ike, respondents
to TranStar survey indicated 17%
consulted friends and relatives;
most relied on the news and
internet .

## Slide 20: Transportation Related Improvements Used During Ike
Discouraged non-essential trip the day before
and during mandatory evacuation
High percentage shelter-in-place
Considerable resources to evacuate
special needs populations early
  ▫ Texas Military Forces, C-130 aircraft
  ▫ 900+ buses, 500+ ambulances,
  100 paramedic buses, 350 accessible vans
  ▫ Multi-state agency involvement
  ▫ Activating shelter network
    about 80 locations

## Slide 21: Lessons Learned in 2008
Work done since Rita was helpful
  ▫ ITS deployments gave us eyes outside of Houston
  ▫ Mutual assistance agreements (especially shelters and movement of special needs)
  ▫ Zip-zone maps / public information about evacuation zones worked better
  ▫ Message of “hide from the wind, run from the water” generally heeded

## Slide 22: Voluntary Survey* Hurricanes Rita and Ike
For Ike
  ▫ 23% of respondents evacuated, so 77% sheltered in place.
▫ 25% indicated their delay was less than 1 hour;
other categories of responses were all fewer than
10%.
* Web based on TranStar Website, Not Statistically Validated; N = 416 to 475 for Ike, depending on the question; 11,960 to 14,664 for Rita.

## Slide 23: Voluntary Survey* Hurricanes Rita and Ike
Question | Rita | Ike
Number Respondents | 6570 | 1788
Experienced No Evacuation Problems | 6% | 54%
Problem with Fuel Availability | 25% | 8%
Problems with Traffic | 24% | 34%

## Slide 24
Traveler behavior difficult to predict (Peacock et. al.,2007; Murray-Tuite and Mahmassani, January 2005)
  ▫ Evacuate or Shelter in Place
  ▫ Follow the evacuation zones
Reality compared to perception about evacuation
Hurricane Ike Revisited:
Questions Remaining

## Slide 25: Shelter in Place or Evacuate
Decide Ahead and Make Plans

## Slide 26: Shelter in Place or Evacuate
Plan Prior to a Weather Event
If in a Storm or Surge Area, Monitor Closely
Determine the Limits of Your Home
  ▫ Children
  ▫ Elderly
  ▫ Special Needs
If evacuating, follow the zonal categories

## Slide 27: References
Church, Richard L. and Ryan Sexton (April 2002). Modeling Small Area Evacuation: Can Existing Transportation Infrastructure Impede Public Safety? California Department of Transportation, Testbed Center for Interoperability, Task Order 3021.
FEMA Appendix F: Hurricane Evacuation Models and Tools (web address?)
IEM, Inc. Products and Services Planning. Transportation/Evacuation Analysis www.ieminc.com/Products_andServices/transportation_evacuation%20modeling.htm (retrieved 7/10/07)
Murray-Tuite and Hani Mahmassani (January 2005). Identification of Vulnerable Transportation Infrastructure and Household Decision Making Under Emergency Evacuation Conditions. Southwest Region University Transportation Center. 167528-1
Peacock, Walter et. al., (January 18, 2007) Draft: Hurricane Rita Behavioral Survey Final Report. Hazard Reduction and Recovery Center, Texas A & M University. Texas Department of Transportation.
Radwan, Essam et. al., (April 2005). Framework for Modeling Emergency Evacuation. Center for Advanced Transportation Systems Simulation. Contract BD548, RPWO #5.